This document explains how the Potential Temperature and the Water Vapor Mixing Ratio was estimated for each of the plot.

Potential Temperature: (Poisson’s equation)

Po = standard pressure = 1000hPa

P = existing pressure or pressure at an specific height

RRd = gas constant = 287 J K-1kg-1

cp = specific heat at constant pressure = 1004 J K-1kg-1

T = existing temperature in Kelvins (K)

Water Vapor Mixing Ratio:

(1)

Last equation (1) is used to calculate the water vapor mixing ratio, in order to get this the value, the saturation mixing ration () has to be calculated.  The saturation mixing ratio is calculated as followed:

(2)

To obtain the saturation mixing ratio value (2), the saturation vapor pressure () has to be calculated too. The saturation vapor pressure is calculated with the next equation:

(3)

where A = 2.53×108 kPa and B = 5.42 ×103 K.

Another equation to calculate the saturation vapor pressure is:

(4)

where To = 273.15 K and T is the current temperature in Kelvins.

# Footnotes

Wallace, John M., Peter V. Hobbs, 2006: Atmospheric Science: An Introductory Survey, 2nd ed. Academic Press, pp. 77,78.

Wallace, John M., Peter V. Hobbs, 2006: Atmospheric Science: An Introductory Survey, 2nd ed. Academic Press, pp. 80-82.

Rogers, Roddy R., Man K. Yau, 1996: A Short Course in Cloud Physics, 3rd ed. Butterworth-Heinemann, pp. 14.